## Slide 1
NGSTability — Next Gen PCM Buck Converter
Stability Analysis & PID Optimization
Digital Control Loop Modeling | RTL-Accurate Coefficients | Global Optimization | AMS Correlation

## Slide 2
Why NGSTability? — Motivation
New architecture: moved from voltage-mode analog compensation to PCM buck with digital PID
→ Entirely different control loop — no legacy model or design methodology to reuse
The gaps we faced:
• No accurate model to predict which K1/K2/K3 PID sets produce a stable loop
• PID tuning was done manually by trial-and-error — both in lab and in AMS simulation
• Even after finding a stable set, we had no visibility into actual PM/GM margins
• Pre-silicon: each AMS trial takes hours — searching for a stable set is painfully slow
NGSTability approach:
1. Model the full closed-loop system in MATLAB (Laplace domain)
→ Bode plot → extract GM, PM, crossover frequency in milliseconds
2. Validate: if MATLAB predicts stable, it should correlate with lab and AMS measurements
3. Once the model is trusted, run global optimization over all possible PID sets
→ Find the best K1/K2/K3 under stability and hardware constraints automatically
4. Replaces days of manual AMS iteration with minutes of automated search

## Slide 3
1. Small-Signal Modeling — PCM Feedback Loop Architecture
Block | Transfer Function | Key Parameters
PCM Plant | Gvc = Hdc · Fp · Fh | L=0.47µH, C=22µF, Resr=3mΩ
Digital PID | Hpid = Kp + Ki/s + Kd·s/(Tf·s+1) | After >>6 shift
ADC delay | Padé(5ns, order 2) | 4-bit, 80mV window
DAC filter | 1 / (1 + s/ωdac) | 500 kHz pole, 12-bit
Blanking + Comp delay | Padé(15ns + 8ns) | 
Feedback | H = β = 0.5 | Resistive divider

## Slide 4
1. Small-Signal Modeling — PCM Plant: Control-to-Output
Gvc(s) = Hdc · Fp(s) · Fh(s)
Hdc = (R/Ri) · 1/(1 + R·Ts·(mc·D'−0.5)/L) → DC gain, load-dependent
Fp(s) = (1 + s·C·Resr) / (1 + s/ωp) → output filter pole + ESR zero
Fh(s) = 1 / (1 + s/(ωn·Qp) + s²/ωn²) → sampling double pole at fs/2
Slope compensation: mc = 1 + se/sn, se = 0.7 MV/s
Plant gain varies significantly with load current (1 mA – 3 A)
→ Must evaluate stability across the full load range, not just one operating point

## Slide 5
2. Closed-Form Loop Components — Transfer Functions
Analog reference compensator (Type-II):
Hc(s) = (ωp1/s) · (1 + s/ωz,comp) / (1 + s/ωp2)
Digital PID compensator (Laplace domain):
Hpid(s) = Kp + Ki/s + Kd·s / (Tf·s + 1)
Complete digital compensator chain:
Hdig(s) = G_ADC · Hadc(s) · Hpid(s) · G_digital · G_DAC · Hdac(s) · Hblank(s) · e^(-sTd)
Loop gains:
Lc(s) = Hc(s) · Gvc(s) · H (analog reference)
Lloop(s) = Hdig(s) · Gvc(s) · H (digital loop gain)
Closed-loop transfer function:
Tloop(s) = Lloop(s) / (1 + Lloop(s)) (feedback(Lloop, 1))
Delays → 2nd-order Padé | G_digital = 1/64 | ADC/DAC gains = 1

## Slide 6
2. Phase Budget at Crossover (fc = 600 kHz)
Block | Phase Contribution | Notes
Plant × H | ~ −XX° | Load-dependent
ADC delay (5 ns) | ~ −X° | Padé model
Digital PID | ~ +XX° | Phase boost from zeros
DAC filter (500 kHz) | ~ −X° | Single pole
Blanking delay (15 ns) | ~ −X° | Padé model
Comp delay (8 ns) | ~ −X° | Padé model
TOTAL | ~ −XXX° | 
Phase Margin | PM = Total + 180° | Target ≥ 35°

## Slide 7
3. RTL-Accurate Coefficient Mapping
Three equivalent representations of the same controller:
Lab Position [P, I, D] ↔ RTL [K1, K2, K3] ↔ Effective [Kp, Ki, Kd]
Lab → RTL: K1 = P+I+D, K2 = −P−2D, K3 = D
RTL → PID: Kp = −K2−2K3, Ki = (K1+K2+K3)/Tctrl, Kd = K3·Tctrl
Effective: Kp_eff = Kp · G_digital, Ki_eff = Ki · G_digital, Kd_eff = Kd · G_digital
RTL PID recursion (velocity form):
u[n] = u[n−1] + K1·e[n] + K2·e[n−1] + K3·e[n−2]
output = (u >> 6) + 2048
All conversions are invertible — any representation maps to any other

## Slide 8
3. Hardware Constraints on PID Design Space
Coefficient | Bit Width | Range | Constraint
K1 | 20-bit signed | ±524,287 | ¦K1¦ ≤ 2^19 − 1
K2 | 20-bit signed | ±524,287 | ¦K2¦ ≤ 2^19 − 1
K3 | 11-bit signed | ±1,023 | ¦K3¦ ≤ 2^10 − 1
PID accumulator | Pre-clamp | −131,072 to +131,008 | RTL MIN/MAX_VALUE
PID output | 12-bit unsigned | 0 – 4,095 | After >>6 + 2048 offset
Ki resolution | ~4×10⁶ LSB | Coarse steps | Integer I_cmd quantization

## Slide 9
4. Global PID Optimization — Architecture
Goal: Find [Kp, Ki, Kd] maximizing stability + transient performance across 9 loads
Search space (log10 scaled):
Kp ∈ [0.016, 10000] Ki ∈ [4×10⁶, 5×10⁸] Kd ∈ [Kd_min, Kd_max]
Load sweep: Iload = [1mA, 100mA, 300mA, 500mA, 700mA, 900mA, 1.1A, 2A, 3A]
Two-stage optimizer:
1. PSO (Particle Swarm) — 40 particles × 80 iterations → global exploration
2. Nelder-Mead hybrid refinement → local polishing of best PSO result
Hard constraints:
• Closed-loop stable at ALL load points
• PM ≥ 35°, GM ≥ 6 dB at every load
• K1/K2/K3 within RTL bit-width (200-point penalty per overflow)

## Slide 10
4. Multi-Metric Cost Function
cost = −score + overflow_penalty
Score = stability margins + load-step transient (all in one sum):
score = 2·PM_min + 1·GM_min + 0.15·PM_avg + 0.1·GM_avg − 1·|log₁₀(fc/fc_target)|
+ 12 · min(slew / 0.002, 10) ← reward fast recovery
− 12 · t_settle / 5µs ← penalize slow settling
− 12 · ΔV_undershoot / 20mV ← penalize deep voltage dip
All terms contribute to a single score — optimizer maximizes the total
Margin caps: PM capped at 85°, GM capped at 40 dB
Overflow penalty: +200 per K1/K2/K3 exceeding RTL bit-width
Convergence visualization: cost vs iteration with PSO → fminsearch transition marker

## Slide 11
5. Optimized Digital Loop vs Ideal Analog Compensator
Metric | Analog (Ideal Hc) | Digital (Optimized) | Notes
Compensator type | Type-II continuous | Velocity PID (K1/K2/K3) | 
Phase Margin | XX° | XX° | Fill from simulation
Gain Margin | XX dB | XX dB | Fill from simulation
Crossover freq | 600 kHz | ~XXX kHz | Target = fs/10
Phase loss sources | None | ADC/DAC/blanking delays | 10–20° typical loss
Quantization | Infinite resolution | Integer K1/K2/K3 | Finite bit-width
Load robustness | Single operating pt | 9 loads simultaneously | 1mA to 3A

## Slide 12
5. 3D Stability Design Space Visualization
Axes: Kd (X), Ki (Y), Kp (Z) — log-scaled
GREEN = stable at ALL 9 load points (PM ≥ 35°, GM ≥ 6 dB)
RED = unstable or insufficient margins at any load point
BLUE STAR = optimizer's selected solution
Key insights:
• The stable region is a bounded volume — not all PID combinations work
• Optimizer solution sits inside the stable region, near the best-margin boundary
• Boundaries shift with load current — multi-load check is essential
2D projections (Kd-Ki, Kd-Kp, Ki-Kp) show the stable envelope for each pair
→ Green if stable for ANY value in the collapsed axis
Grid: 25 × 25 × 15 = 9,375 points evaluated

## Slide 13
6. RTL-Accurate Cycle-by-Cycle Nonlinear Predictor
Feature | Implementation | Details
ADC | 4-bit quantization | 0.36–0.44V window, 16 levels, 5mV/LSB
PID accumulator | Velocity form + pre-clamp | K1·e[n] + K2·e[n−1] + K3·e[n−2]
Shift + offset | >>6 then +2048 | Unsigned 12-bit output
DAC | 12-bit code → analog | NMOS Vth cap at 1.6V (not 1.8V)
DAC filter | 500 kHz analog pole | Discrete IIR at Tctrl
Plant model | State-space @ Tctrl | Control path + load disturbance (parallel)
Load disturbance | Gload = −Zout_OL | Passive output impedance only
Load step | Configurable profile | Delay, rise time, amplitude, width

## Slide 14
6. Validation Pipeline: Predictor → AMS → Silicon
Tiered validation flow:
Optimizer → Nonlinear Predictor → AMS Simulation → Silicon
(fast, 1000s (catches quant/ (full circuit (final
of evals) saturation effects) validation) proof)
Metrics compared at each stage:
• Vout undershoot: target < 20 mV
• Recovery slew: target > 0.002 V/µs
• Settling time: target < 5 µs
• Steady-state Vout: 0.800 V
Why this tiered approach?
→ Linear model: fast optimization (thousands of evaluations in minutes)
→ Nonlinear predictor: catches effects the linear model misses
→ AMS: full circuit-level validation before silicon commitment
→ Saves weeks of AMS iteration time

## Slide 15
Summary — NGSTability Methodology
1. Small-signal Laplace-domain model of the PCM feedback loop
→ Closed-form plant, digital blocks, delays — all analytically derived
2. RTL-accurate coefficient mapping (K1/K2/K3 ↔ Lab P/I/D ↔ Kp/Ki/Kd)
→ Exact quantization and bit-width constraints from RTL
3. Global optimization (PSO + Nelder-Mead) across full load range
→ Cost function: PM + GM + crossover + load-step transient metrics
4. 3D stability map visualization of the feasible PID design space
5. Cycle-by-cycle nonlinear predictor for AMS correlation
→ RTL-accurate ADC/DAC quantization, PID clamping, load disturbance
6. Validated pipeline: Linear model → Predictor → AMS → Silicon
→ Each tier catches progressively finer effects while managing compute cost